## Slide 1: Accountability in Hosted Virtual Networks
Eric Keller, Ruby B. Lee, Jennifer Rexford
Princeton University

## Slide 2: Motivation
Trend towards hosted virtualized infrastructures
  Enables companies to easily deploy new services
  e.g., Amazon EC2
Hosted virtual networks
  Infrastructure provider: owns/maintains routers
  Service provider: leases slices of routers

## Slide 3: Understanding Security Threats
Service Provider wants
  Control software running exactly as written
  Data plane forwarding/filtering as instructed
  Data plane performing with QoS promised
  Confidentiality/Integrity of data
  Availability
Infrastructure Provider
  Doesn’t want to be unjustly blamed
Next: How are these possibly compromised

## Slide 4: Old model: Owning the router
Routing
Processes
Line
Card
Line
Card
Interconnect
OS
FIB1
FIB1
Routing
Processes
NIC
NIC
Interconnect
OS
fwd
FIB1
Hardware-based router
Software-based router
Entire platform is trusted

## Slide 5: New model: Hosted (threat 1)
Routing
Processes
Line
Card
Line
Card
Interconnect
OS
FIB1
FIB1
Virtualization layer
Routing
Processes
NIC
NIC
Interconnect
OS
Virtualization layer
fwd
FIB1
Infra. Provider can tamper with control software,
  data plane configuration (HW router),
  data plane implementation (SW router)
Hardware-based router
Software-based router
Service
provider
Infra.
provider
fwd
FIB1

## Slide 6: New model: Shared (threat 2)
Routing
Processes
Line
Card
Line
Card
Interconnect
OS
Routing
Processes
OS
FIB1
FIB2
FIB1
FIB2
Virtualization layer
Routing
Processes
NIC
NIC
Interconnect
OS
Routing
Processes
OS
Virtualization layer
fwd
FIB1
FIB2
Hardware-based router
Software-based router
Service
providers
Infra.
provider
Pink service provider can attack virtualization layer
  Possible competitor of Blue service provider
  Affect operation of Blue service provider

## Slide 7: Accountability
Security threats lead to the need for accountability
Accountable: Subject to the obligation to report, explain, or justify something; responsible; answerable [Random House]
In hosted virtual infrastructure…
  promised in the Service Level Agreement (SLA)

## Slide 8: Outline of Approaches
Detect
  Network Measurement
Prevent
  Advances in Processor Architecture
For each
  Present solution possible today
  Propose extension

## Slide 9: Outline of Approaches
Detect
  Network Measurement
Prevent
  Advances in Processor Architecture
For each
  Present solution possible today
  Propose extension

## Slide 10: Monitoring SLA compliance
Probe to determine:
  Loss rates
  Latency/Jitter
  Path taken
To know how DP supposed to act:
  Log control messages (at boundaries)
  Model network and replay logs

## Slide 11: Extending the Interface Card
Logging at edge -> expensive to simulate
  Log control messages at each interface
Probing at edge -> pinpointing difficult
  Sampling at each interface (using secret key)
Probing at edge -> complete path unknown
  Bloom filter at each interface to store whether or not a particular packet went through this interface
Measurement by service provider -> can’t prove violation (is it the service provider’s fault)
  Place trust in interface card vendor for logging (e.g., private key of vendor signs the logs)

## Slide 12: Outline of Approaches
Detect
  Network Measurement
Prevent
  Advances in Processor Architecture
For each
  Present solution possible today
  Propose extension

## Slide 13: Trusted Platform Module
Recall what service provider wants
  Control software running unmodified
  Data plane acting as instructed
  Data plane performing with correct QoS
  Confidentiality/Integrity of data
TPM: Chip on motherboard (on chip in future)
  Encrypting storage
  Attesting to integrity of system

## Slide 14: TPM Limitations
Does not protect against dynamic attacks
  Can’t ensure software running unmodified
Relies on chain of trust
  Control processes verified by virtualization layer
  Can’t know if data plane acting as instructed with QoS (SW - Data plane is in virtualization layer) (HW – Configuration goes through virtualization layer)
  Confidentiality of data not addressed

## Slide 15: TPM needs physical separation
Remote control plane
  e.g., Ethane/NOX, 4D
Routing
Processes
NIC
NIC
Interconnect
OS
Routing
Processes
OS
Virtualization layer
fwd
FIB1
FIB2
Routing
Processes
NIC
NIC
Interconnect
OS
OS
fwd
FIB1
FIB2
Minimal controller
TPM
Routing
Processes
OS
TPM
TPM
3rd Party Data Plane

## Slide 16: Security Enhanced Processor
TPM relies on physical separation
Instead – extend processor architecture
  Confidentiality/integrity of data and software
  Encryption/decryption to/from memory
  Examples: SP[ISCA05], AEGIS[MICRO03], XOM[ASPLOS00]
  Minimal extra circuitry
None designed for hosted/shared environment
None made good business case
  So no (very limited) success
  Market size of hosted virtualized infrastructures provides the incentive

## Slide 17: Base Processor
Main Memory
Processor
cache
CPU

## Slide 18: Trust Vendor
Device
key
Main Memory
Processor
cache
CPU
Vendor: Install private device key
(write only, configured in vendor’s facility)

## Slide 19: Don’t trust infrastructure provider
Install
key
K0
K1
K2
K3
Device
key
Main Memory
Processor
cache
CPU
slot
0xf918
0x1234
Service Provider: Install secret key

## Slide 20: Protecting software and data
Install
key
K0
K1
K2
K3
Device
key
Main Memory
Processor
cache
CPU
slot
0x1234
encrypt/
decrypt
slot
0xde21f19
0x18
0x12aaa22
0xfe
0xde21f19
0x18
0xde21f19
Encrypt/Decrypt data to/from memory
(or just hash/verify)

## Slide 21: What’s the right approach?
 | Measure | +NIC | TPM | vm-SP
Trust | Other infrastructure providers | Vendor | Vendor | Vendor
Run-time complexity | High | Medium | Low | Low
Confidentiality | No | No | Yes | Yes
Main downside | Accuracy vs computation / storage tradeoff | Need to extend interface card | Requires physical separation | Need general purpose processor extension
Virtual Mode-SP (extended processor) provides protection desired, minimal complexity, with business incentives to make it reality.

## Slide 22: Conclusion
A step toward realizing hosted virtual networks
New business model leads to new security issues
  Platform is hosted and shared
Can use monitoring to detect violations
Better to rearchitect routers to prevent violations
Future work:
  Virtual Mode-SP for hosted virtualized infrastructures
  Explore implications of trusting the vendor